## Slide 1
Development and Applications of Air Benefit and Cost and Attainment Assessment System (ABaCAS)
Science
Policy
Actions
Cost/Benefit & Attainment
ABaCAS
Air Pollution
(PM2.5 & O3)
Emissions Control & Cost
Health & Economic
Benefit
AQ
Benefit & Attainment
Carey Jang, Ph.D.
Office of Air Quality Planning & Standards
U.S. EPA, 12/6/2019

## Slide 2: Outline
Air Benefit & Cost and Attainment Assessment System:
  “ABaCAS ”: An integrated assessment model developed by a team of international scientists; key components including:
    “ICET”: Control Cost Estimate Tool
    “RSM/CMAQ”: Air Quality Assessment Tool
    “SMAT-CE”: Attainment Assessment Tool
    “BenMAP-CE”: Health & Economic Benefit Tool
    “LE-CO”: Least Cost Optimizer Tool (prototype)
Evolution & Recent Development:
  1. ABaCAS Prototype (2016): Cost/Benefit & Attainment Assessment
  2. ABaCAS 1.x (2017): Connected under One Integrated Platform
  3. ABaCAS 2.x (2018): ABaCAS Streamlined Edition (ABaCAS-SE)
  4. ABaCAS 3.x (2019): ABaCAS Optimized Edition (ABaCAS-OE)
  5. ABaCAS 4.x (2020): Develop New Tool (FAST-CE) & Enhance RSM-VAT

## Slide 3
Optimized Edition
“ABaCAS-OE”
Optimized (least-cost) control strategy
Least Cost Optimizer “LE-CO”
Polynomial Functions “pf-RSM” and “i-RSM”
ABaCAS
Prototype
ABaCAS 1.x
ABaCAS 2.x
Four Key Tools:
Cost estimate
AQ Benefit
AQ Attainment
Health Benefit
ICET
BenMAP-CE
SMAT-CE
RSM-VAT
2015
Integrated
Platform
Integrated cost/benefit assessment
International applications
ABaCAS website
ABaCAS training & User’s Guides
2016
Streamlined Edition
“ABaCAS-SE”
Streamlined cost/benefit assessment
China & USA pilot cases
Model-VAT Visual Tool
Data Fusion Tool
2017
2018
ICET
ABaCAS 3.x
2019

## Slide 4
Control
& Cost
Estimate
Real-time
Air Quality
Benefit
Air Quality
Attainment
Assessment
Health &
Economic
Benefit
Integrated
Cost/Benefit
& Attainment
Assessment
ABaCAS : Air Benefit and Cost & Attainment Assessment System
Integrated AQ Decision Support System (http://www.abacas-dss.com)
“ABaCAS 1.0”
2016

## Slide 5: “ABaCAS”: Air Benefit and Cost & Attainment Assessment System
An integrated AQ Decision Support System (v. 3.x)
5
Developed for “Scientists” and “Policy Makers”

## Slide 6: ICET: International Control cost Estimate Tool
Provide Control Cost Analysis and Estimate : A flexible & modular control & cost estimate tool to give an estimate of control cost and link to RSM/CMAQ & BenMAP-CE for control cost/benefit assessment
ICET
(International Emissions Control Cost Interface Tool)
Notes: Comment: This is an important slide, but needs to be improved. Consider to use animations to highlight the key features & differences

## Slide 7: RSM: Response Surface Model
Base
Control
Provide Real-time AQ Response of Emissions Control:
A cutting-edge tool developed by USEPA & ABaCAS team to provide real-time response of AQ concentrations to changes in emission sources
RSM-VAT:
(RSM Visualization &
Analysis Tool)
RSM/CMAQ
Notes: Comment: This is an important slide, but needs to be improved. Consider to use animations to highlight the key features & differences

## Slide 8: SMAT-CE: Software for Model Attainment Test
Developed by EPA and “ABaCAS” team to perform attainment assessment for EPA’s national rules and SIPs on PM2.5, O3 & Visibility
“SMAT-Asia” has been developed for customized Asian applications
SMAT-CE
(Community Edition)
(Community Edition)
Notes: Comment: This is an important slide, but needs to be improved. Consider to use animations to highlight the key features & differences

## Slide 9: BenMAP-CE: Environmental Benefit Mapping & Analysis (Community Edition)
Provide Health Impacts & Economic Benefits Estimate:
Developed by EPA and “ABaCAS” team to estimate health & environmental impacts and economic benefits occurring changes in air quality
BenMAP-CE
(Community Edition to
Replace Legacy BenMAP)
BenMAP-CE
Notes: Comment: This is an important slide, but needs to be improved. Consider to use animations to highlight the key features & differences

## Slide 10: “ABaCAS-SE” and “ABaCAS-OE”
An integrated AQ Decision Support System (v. 3.x)
10
Developed for “Scientists” and “Policy Makers”

## Slide 11: “ABaCAS-SE”: (Streamlined Edition”, 2017)
Cost estimate ($$)
Health Benefit ($$)
Attainment (DVs)
AQ Benefit (ug/m3)
Benefit ($$)/Cost ($$)
> 12 ug/m3 (non-attainment)
ICET script
BenMAP-CE script
SMAT-CE script
RSM-VAT script
ICET
BenMAP-CE
SMAT-CE
ABaCAS-SE Master Script
RSM-VAT
BenMAP-CE
ABaCAS-SE
Control Strategy
B
Control Strategy
C
……………
Control Policy Scenarios
Control Strategy
A
Streamlined Assessment
ICET
Benefit/Cost = ~20
Notes: spatial field: A Spatial Field refers to air pollution estimates made at the center of each grid cell in a specified modeling domain. For example, MATS might calculate ozone design values for each grid cell in the modeling domain. Several types of Spatial Fields can be calculated for ozone and PM.
利用环境监测数据、模型数据（主要是CMAQ模拟的结果）作为模型输入，并利用优化的数理统计技术对大气复合污染状况进行模拟，实现对环境空气质量标准的达标评估。其中包括point estimate和spatial field estimate。

## Slide 12: China YRD “2030” PM2.5 Case
RSM/CMAQ
BenMAP-CE
SMAT-CE
Benefit/Cost
(5~10 minutes to run)
Benefit/Cost =~ 9.3

## Slide 13: Western U.S. Case Study (ABaCAS-SE)
CMAQ (no-RSM)
BenMAP-CE
SMAT-CE
Benefit/Cost
(PI: UNC-IE)
Benefit/Cost =~ 18

## Slide 14: “ABaCAS-OE”: Optimized Edition (2019 Prototype)
14
Developed for “Scientists” and “Policy Makers”

## Slide 15: “ABaCAS-OE ” (2019) (Optimized Edition”: under “ABaCAS 3.x”)
Attainment
Target
Health Benefit ($$)
Optimized Control & Cost for Attaining AQ Goals
Benefit ($$)/Cost ($$)
> 12 ug/m3 (non-attainment)
ABaCAS-OE
Pollutant B: O3
attains 80 ppb (MDA8)
Attainment Goals
Pollutant A: PM2.5
attains 35 ug/m3 (annual)
Optimized Control Strategy
SMAT-CE
ICET
pf-RSM
BenMAP-CE
LE-CO
Control Cost
Optimizer
Air Quality
Benefit
Control &
Cost Estimate
Benefit/Cost = ~20
Notes: spatial field: A Spatial Field refers to air pollution estimates made at the center of each grid cell in a specified modeling domain. For example, MATS might calculate ozone design values for each grid cell in the modeling domain. Several types of Spatial Fields can be calculated for ozone and PM.
利用环境监测数据、模型数据（主要是CMAQ模拟的结果）作为模型输入，并利用优化的数理统计技术对大气复合污染状况进行模拟，实现对环境空气质量标准的达标评估。其中包括point estimate和spatial field estimate。

## Slide 16: ABaCAS-OE: China Jinan “PM2.5 & O3” Case
SMAT-CE
RSM-VAT
LE-CO
ICET
PM2.5 Attainment Goal: 60 ug/m3
O3 Attainment Goal: 160 ug/m3 (~80 ppb)
Optimized Control Share & Reduction Share
Emissions Control
& Cost
AQ Reduction &
Source Contribution

## Slide 17: ABaCAS-OE: China Jinan “PM2.5 & O3” Case
SMAT-CE
RSM-VAT
LE-CO
ICET
PM2.5 & O3
Attainment Goals
Optimized Control Cost Share for both PM2.5 & O3
Emission & Control Cost
Reduction & Source Contribution
Primary PM2.5
NH3
VOC
SO2
NOx

## Slide 18: ABaCAS-OE: China Jinan “PM2.5 & O3” Case
SMAT-CE
LE-CO
PM2.5 & O3
Attainment Goals
PM2.5 Reduction Share
O3 Reduction Share
Primary PM2.5
NH3
VOC
SO2
NOx
P. PM2.5
NH3
VOC
SO2
NOx
Control Cost Share
for both PM2.5 & O3

## Slide 19: ABaCAS-OE: China Jinan “PM2.5 & O3” Case
SMAT-CE
RSM-VAT
LE-CO
ICET
PM2.5 & O3
Attainment Goals
Control Cost Curve
PM2.5 Reduction &
Source Contribution
Emissions Reduction
(base vs. control)
O3 Reduction &
Source Contribution

## Slide 20: ABaCAS-OE: China Jinan “PM2.5 & O3” Case
SMAT-CE
RSM-VAT
LE-CO
ICET
PM2.5 & O3
Attainment Goals
BenMAP-CE
Benefit/Cost
Benefit/Cost =~ 11
Mortality
Valuation

## Slide 21: “ABaCAS”: Air Benefit and Cost & Attainment Assessment System Analytical Tools in “ABaCAS 3.x” (2018-2019)
New Analytical Tools: “Model-VAT” & Data Fusion Tool

## Slide 22
Model-VAT:
Multi-Scale Model Visualization & Analysis Tool
H-CMAQ
(hemispheric)
GOES-Chem
(global)
User-Friendly V/A & Eval. Tool for Photochemical & Dispersion Models
CMAQ/ CAMx
(regional)
(Easy Map Transformation)

## Slide 23
Model-VAT: Multi-Scale Model V/A Tool
PM2.5 (July 2016)
O3 (July 2016)
H-CMAQ (108km)
GEOS-Chem (4ox5o)
CMAQ (36-km)

## Slide 24
Model-VAT: Model Analysis & Evaluation
Remote File Access
Flexible
Data
Output
Link to “R”

## Slide 25: “Data Fusion” Tool (Fusing Model and Monitor and/or other data)
Inputs:
Model & Monitor or other data
(dispersion model, satellite data, LUR, etc.)
Spatial: grid & non-grid (census)
Temporal: annual/monthly/daily
Data
Fusion
Open-Source & User-Friendly
Techniques:
eVNA, VNA,
Downscaler, etc.
Method Development, Evaluation & Research
BenMAP-CE
Health Studies
SMAT-CE
Attainment Test
Regulatory Assessment
(PM & O3 RIA, REA)
Cross-Validation
(QA, Multi-fold, Leave-one-out, etc)
Notes: In a simple team, DFT. An important last step of regulatory modeling and other assessment

## Slide 26
Li et. al., 2019, J. of Environ. Management
“Data Fusion” Tool: Application in China PRD (Fusing Model and Monitor data)
Model Data
Monitor Data
Fused Data
Health Benefits
Jim KELLY (next talk): “Data Fusion Tool application for PM2.5 spatial fields in USA”

## Slide 27
  “FAST-CE”: Flexible AQ Scenario Tool - CE
  A user-friendly and open AQ assessment tool for source contribution analysis/visualization/evaluation
  Allow to adjust AQ surface and provide scenario analysis for source contribution assessment methods such as “OSAT/PSAT/APCA/ISAM, DDM, and RSM”
  RSM-VAT:
    Update pf-RSM w/ differential method & add i-RSM
    GUI re-design and upgrade
  Model-VAT: add “Model Evaluation” module
  Data Fusion Tool: add advanced DF methods & dataset
“ABaCAS 4.x”: Work Plan (2019-2020)

## Slide 28: FAST-CE: “Flexible Air Quality Scenario Tool – Community Edition”(2019-2020)
Source Apportionment Modeling
Source Contribution Analysis
(SA/RSM/DDM)
Chemical approximation
Math. & Chemical approximation
FAST-CE
DDM
RSM
Math. approximation
Source/Receptor Sensitivity Modeling
Response Surface Modeling
OSAT/PSAT/APCA & ISAM
Optimized Cost/Benefit Control Strategies
Least cost strategies (LE-CO)
Attainment assessment tool (SMAT-CE)
Health benefit tool
(BenMAP-CE)
Assessment of health & economic benefit and attainment benefit
Photochemical model (CMAQ/CAMx)
International cost estimate (ICET)
Dynamic control
strategies
Emission Inventory
(regions, pollutants, sectors, etc.)
Emission control factors, etc.
Multiple tracer species
Photochemical model (CAMx/CMAQ)
Input parameters
Sensitivity coefficients

## Slide 29: New RSM Development:“pf-RSM”&“i-RSM”
AQM
Air
pollutant
Emissions
Single scenario
Air Quality Model
(CMAQ, CAMx, etc.)
U.S.EPA
ERSM
Air
Region C
Region B
Region A
Region A
Region B
Real-time pollutant responses
to multi-region sources
•
Chemistry
•
Transport
•
Indirect
Multi-Region
Extended RSM
Tsinghua U.
RSM
Air
pollutant
Emissions
Change
Real-time pollutant responses
to emissions change
Response Surface
Model
U.S.EPA
Pf-RSM
Emis./Reg. C
Emis./Reg. B
Emis./Reg. A
RSM w/
Polynomial Functions
Tsinghua U./SCUT
Pollutant A (PM)
Pollutant B (O3)
RSM w/
Temporal
Polynomial
Functions
Pollutant A (PM)
Pollutant B (O3)
Pollutant A (PM)
Pollutant B (O3)
Multi-pollutant responses
based on polynomial functions

## Slide 30: “pf-RSM” Methodology
“pf-RSM”: Response Surface Model based on Polynomial Functions
(Temporal & multi-region RSM)
Chemistry:
Degree of
Non-linearity
Chemistry:
Term of
Interactions
Model:
Only 3rd step involved in training samples (i.e., model runs), and thus significantly reduces
# of model runs required for accuracy
Xing et. al., 2018,
Atmos. Chem. & Phys.
Polynomial Functions
2nd next talk by Prof. Jia Xing

## Slide 31: Machine Learning “i-RSM”
“i-RSM”: “Indicator-based CNN pf-RSM”
Xing et. al., 2019, in preparation
Traditional RSM | pf-RSM | i-RSM
>100s | 20~30 | 2
# of model runs needed for maintaining RSM accuracy in predicting control responses for each selected study region
Use
pre-defined
“Indicators”
for
PM2.5 (18)
& O3 (16)
to predict
nonlinearities
of species
and their interactions

## Slide 32
“ABaCAS” Website (www.abacas-dss.com)
Everything you need is here! “abacas-dss.com”

## Slide 33
Carey Jang, U.S. EPA, Jang.carey@epa.gov
THANK YOU!
www.ABaCAS-dss.com

## Slide 34: 2018 ABaCAS/CMAS Conference/Training Workshop (Beijing, 5/21-23)
2019 ABaCAS Conference/Training Workshop (Hangzhou, 5/19-22)

## Slide 35: RSM: real-time estimate of air quality responses
Ambient Concentration
Emission ratio
0
1
“real atmosphere”
Sensitivity (e.g., DDM)
Source Apportionment (e.g., ISAM)
RSM
base
Response Surface Model (RSM)
——a meta-model built upon multi-“Brute Force” model simulations, to explore the response relationship between emission changes and air quality responses

## Slide 36
Photochemical
model (CMAQ/CAMx)
Source Apportionment Modeling
Grouped by pollutants, source categories and source regions
Performance Evaluation for Source Contribution Analysis Methodologies
Emission Inventory
(regions, pollutants, sectors, BCs, etc.)
Multiple tracer species
Source Apportionment (RSM/DDM//OSAT&PSAT)
Chemical Approximation
Dynamic
control strategies
Emission rates, BCs/ICs, etc.
Input parameters
Math. & Statistical approximation
Photochemical
model (CMAQ/CAMx)
FAST-CE response surface
DDM
RSM
Math. approximation
Source/Receptor Sensitivity Modeling
Response Surface Modeling
(Sensitivity coefficients)
OSAT/PSAT & ISAM
FAST-CE: Flexible Air quality Scenario Tool - Community Ed.）
2019-2020 work plan
Notes: Flexible Air quality Scenario Tool – Community Edition:
Integrate source-receptor relationships generated by photochemical transport models applied with instrumented techniques including SA methods.
Provide a fast turnaround for benefits estimation where time does not allow for the application of a specific control strategy to be modeled with a photochemical transport model.

## Slide 37: New direction: i-RSM with Machine Learning
How to further reduce the number of cases required in RSM?
CTM
RSM
ERSMv1.0
ERSMv2.0
Air pollution
Emission
Air pollution
Emission
Air pollution
Emission A
Emission B
Emission C
pollution 1
pollution 2
Emission A
Emission B
Emission C
Specific scenarios
Full range responses
Full range responses to multiregional sources
Multiple pollutant responses to multiregional sources with well-solved indirect effects
Chemistry
Transport
Indirect
pf-RSM
pollution 1
pollution 2
NOx
NH3
SO2
POA
VOC
A series polynomial functions to explicitly represent the nonlinear response
Xing et al., ACP, 2011
Wang et al., ES&T, 2011
Zhao et al., GMD, 2015
Xing et al., ES&T, 2017
Zhao et al., ACP, 2017
Xing et al., ACP, 2018
i-RSM

## Slide 38: Overview of the RSM evolution
A pathway to reduce the number of cases required in RSM
CTM
RSM
ERSMv1.0
ERSMv2.0
Air pollution
Emission
Air pollution
Emission
Air pollution
Emission A
Emission B
Emission C
pollution 1
pollution 2
Emission A
Emission B
Emission C
Specific scenarios
Full range responses
Full range responses to multiregional sources
Multiple pollutant responses to multiregional sources with well-solved indirect effects
Chemistry
Transport
Indirect
pf-RSM
pollution 1
pollution 2
NOx
NH3
SO2
POA
VOC
A series polynomial functions to explicitly represent the nonlinear response
Xing et al., ACP, 2011
Wang et al., ES&T, 2011
Zhao et al., GMD, 2015
Xing et al., ES&T, 2017
Zhao et al., ACP, 2017
Xing et al., ACP, 2018

## Slide 39: IAMs need fast prediction of air quality response to pollution
Complex emissions of sectors
SMAT
CoST
BenMAP
RSM
ABaCAS
Challenge of Air Pollution Control
Complex atmospheric processes
An integrated assessment model system (ABaCAS)

## Slide 40: Design of RSM with polynomial functions
PM2.5
O3
NOx
2nd
3rd
4th
5th
1st
NH3
1st
2nd
3rd
SO2
1st
POA
1st
VOC
1st
2nd
3rd
High order for NOx and VOC
15 coefficients of polynomial terms can be derived from 20~40 samples
Linear behavior for SO2 and POA

## Slide 41: Design of RSM with polynomial functions (pf-RSM)
NOx
VOC
Original training samples
VOC
NOx
Prior knowledge
Regression-based
RSM (Traditional)
NOx
VOC
Ozone response
regression
VOC
NOx
Fewer samples
Fitting-based RSM
(pf-RSM)
fitting
(Xing J. et al. ACP, 2018)
the prior knowledge was characterized as a series polynomial functions
Fewer samples->high efficiency (60% reduction in the sample number)
Easier investigation on the nonlinearity (e.g., peak value, derivative)

## Slide 42: Validation of pf-RSM prediction
CMAQ
pf-RSM
Baseline
ΔCase1 (moderate control)
ΔCase2 (strict control)
PM2.5 (monthly averages in January 2014, unit: µg m-3)
ENOx, ESO2, ENH3, EVOCs and EPOA
case1 : -49%, -45%, -20%, -64%, -20%
case2 : -76%, -79%, -81%, -83%, -73%

## Slide 43: Validation of pf-RSM prediction
CMAQ
pf-RSM
Baseline
ΔCase1 (moderate control)
ΔCase2 (strict control)
O3 (monthly averages of daily 1-hour maxima in July 2014, unit: ppb)
ENOx, ESO2, ENH3, EVOCs and EPOA
case1 : -49%, -45%, -20%, -64%, -20%
case2 : -76%, -79%, -81%, -83%, -73%

## Slide 44
Health/Econ. Benefit
AQ Benefit
AQ benefit/Cost
assessment
“GCAM-ABaCAS”: Conceptual Framework
Integrated Climate-AQ Benefit/cost Assessment
Climate & AQ co-benefit/cost Assessment
ABaCAS
Control cost
RSM/CMAQ
SMAT-CE
BenMAP-CE
Climate/AQ Policies
Air Pollutant
Emissions
Reduction
ICET
GCAM
Radiative Forcing & Global mean temp
Social Cost of Carbon
(CPP, Paris Agreement, etc.)
Input Data
Output Data
GHG
Emissions
Reduction
Global Change
Assessment Model
Attainment Benefit
Climate benefit/Cost
assessment
Development Plan for 2019-2020, PI: Prof. Jia Xing, Tsinghua Univ.

## Slide 45: 2019 ABaCAS Conference Presentations
5/21 (Mon.):
Dale EVARTS: “Role of ABaCAS- Air Quality and Climate”
Carey JANG (USEPA): “ABaCAS Recent Development”
Shuxiao WANG (Tsinghua U.): “ABaCAS Applications in China”
Jim KELLY: “Data Fusion Tool for PM2.5 spatial fields”
Joshua FU (U. of TN): “Least Cost in ABaCAS-Taiwan”
Yun ZHU (S. China U. of Tech) : “pf-RSM” with differential method
5/22 (Tue):
Junghun WOO (Konkuk U.) : “RSM” application in Korean “GUIDE”
Hsin-Chi LAI (CJCU Taiwan): “ABaCAS-Taiwan Development”
Savitri GARIVAIT (KMUTT): “BenMAP-CE application in Thailand”

## Slide 46: 2018-2019 ABaCAS Papers/Publications
“pf-RSM”: “Quantification of the enhanced effectiveness of NOx control from simultaneous reductions of VOC and NH3 for reducing air pollution in the Beijing–Tianjin–Hebei region, China”, Xing, et al., 2018, Atm. Chem. & Phys.
“LE-CO”: “Least-cost control strategy optimization for air quality attainment: A case study of PM2.5 and O3 in China’s Beijing–Tianjin–Hebei region”, Xing, et al., submitted to J. of Environ. Management
“i-RSM”: “An efficient way in quantifying the nonlinear response of air pollution to emission changes with the indicator-based response surface model ”, Xing, et al., in preparation
“DFT”: “Projecting PM2.5 Spatial Fields to Correspond to Just Meeting National Ambient Air Quality Standards”, Kelly, et al., 2019, Atmospheric Environ.
“DFT & BenMAP-CE”: “Health Benefit Assessment of PM2.5 Reduction in Pearl River Delta region of China using a Model-Monitor Data Fusion Approach”, Li, et al., 2019, J. of Environ. Management
BenMAP-CE”: “The Environmental Benefits Mapping and Analysis Program-Community Edition (BenMAP-CE): A tool to estimate the health and economic benefits of reducing air pollution”, Jason et al., 2018 Environ. Modelling & Software

## Slide 47
Source Contribution Analysis for Policy Assessment
Transport rules or Transport SIPS:
  Assess “significant contribution” of sources in upwind states to downwind states
NAAQS Area designations:
  Provide analysis for States to assess impacts from boundaries
Exceptional events demonstrations:
  Assess impacts of special events such as fire
Inform control strategy development:
  O3, PM2.5, Reg haze SIPs & RIAs
Single source Impact assessments:
  PSD/NSR permitting
Sector impact assessments:
  EGU, Transportation, Industrial Boiler, etc.
Characterizing international contribution:
  179b demonstrations
47
Ozone (ppb)
Natural
Local Contribution
Upwind States
International
U.S. EPA Source apportionment modeling for assessing source contributions to PM2.5 & O3 from emissions
Ozone Source Contribution
(example, not to scale)

## Slide 48
  “ABaCAS-OE”: Optimized Edition
  For developing optimized (least cost) control strategies
    “pf-RSM”: New-generation RSM w/ polynomial functions
      Significantly reduce # of model runs and increase accuracy of RSM predictions
      Provide multi-pollutant (e.g., PM2.5 & O3) and temporal (e.g., daily) RSM results
    “LE-CO”: LEast COst control strategy optimizer tool
      Link with “ICET” & “pf-RSM” to calculate optimized emissions control & cost for attaining AQ goals
“ABaCAS-OE” (2018-2019)

## Slide 49: FAST-CE development (2019-2020) Source Contribution/Response Assessment
Assessment of “Contribution” of sources/pollutants
  Source Apportionment Modeling (Chemical approximation)
    CAMx/OSAT & PSAT, CMAQ/TSSA, CMAQ/ISAM, etc.
  Source/Receptor Sensitivity Modeling (Math. approximation)
    Decoupled Direct Method (DDM), Adjoint method, etc.
Assessment of “Response” (control efficacy) of source emissions reduction
  Zero-Out (Brute Force) Modeling
  Response Surface Modeling (RSM) (Stat./Math. approximation)
    Provide “real-time” AQ response of emissions control
    Previous USA applications: REMSAD (PM2.5):2008, CAMx(O3):2009, CMAQ (EGU PM2.5): 2011
    Evolving into Extended RSM (ERSM):2015, Polynomial functions RSM (pf-RSM): 2018

## Slide 50: 2019 ABaCAS Training Workshop Agenda (5/20/2019)
Time | 5/20 (Mon) | Lead
09:00 - 09:40 AM | ABaCAS Overview and Recent Development | Carey JANG (U.S.EPA)
09:40 - 10:20 AM | ABaCAS Applications in China | Shuxiao WANG & Jia XING, (Tsinghua Univ.)
10:20 - 10:30 AM | Break and Prepare for ABaCAS demo | Yun ZHU & Shichen LONG (SCUT)
10:30 - 12:00 PM | ABaCAS-SE & -OE China Cases Demo/Hands-on | Yun ZHU & Shichen LONG (SCUT), Carey JANG (U.S.EPA)
12:00 - 1:15 PM | Lunch break/discussion | 
1:15 - 2:00 PM | BenMAP-CE: Health & Economic Benefit Assessment - Overview & Demo/Hands-on | Jiandong WANG (Max Planck Inst. for Chem.)
2:00 - 2:45 PM | SMAT-CE: AQ Attainment Assessment - Overview & Demo/Hands-on | Yun ZHU & Shichen LONG (South China Univ. of Technology)
2:45 - 3:00 PM | Break/Discussion | 
3:00 - 4:30 PM | RSM-VAT: Real-time AQ Response to Emissions Control - Overview & Demo/Hands-on | Yun ZHU & Shichen LONG (SCUT)
4:00 - 4:45 PM | Model-VAT: Visualization & Analysis Tool and Data Fusion Tool (DFT): Demo/Hands-on | Yun ZHU & Shichen LONG (SCUT)
4:45 - 5:15 PM | Discussion & Q/A of ABaCAS System and Tools | All

## Slide 51
“ABaCAS” Project Team

## Slide 52: LE-CO: Least-Cost Control Strategy Optimizer
International
cost
estimate tool (ICET)
Response surface
model (RSM)
Marginal Cost Curves
Real-time AQ responses
Target
Control strategies
Control effectiveness
LEast
-
COst
control strategy
optimization
Attainment
goals
Emissions
control cost
Optimize
Optimized/cost-efficient strategy to meet attainment goals
LE-CO
pf-RSM
ICET
SMAT-CE
Xing et. al., 2019, Submitted to JEM

## Slide 53
China PM2.5 Attainment Goals
PM2.5: BTH (Beijing) the worst, YRD (Shanghaiai) median, and PRD (Guangzhou) better.
BTH
YRD
PRD
Others
National Control Plan Goals
(大气国十条: 2013 - 2017)
2013 Annual Avg.
A Major Success:
From 2013 to 2017, Beijing PM2.5 (annual avg.) dropped from ~90 to ~58 mg/m3; PRD is already in attainment
Non-Attainment cities dropped from >95% to ~66%

## Slide 54
AQ Improvements in China’s Key Regions
PM2.5 concentrations
PM2.5 reduction ratio, %
JJJ YRD PRD Beijing
PM2.5 has been significantly improved from 2013 to 2017,
But still exceeded the NAAQS grade II (35 µg/m3) except PRD region
It is also important to further reduce the PM2.5 pollution
How about Ozone?
BTH
YRD
PRD
Others

## Slide 55
2013- RSM, SMAT
2015- BenMAP-CE
2017- pf-ERSM, ICET, LECO
Beijing-Tianjin-Hebei
2012- ICET, RSM, SMAT, BenMAP-CE
2017- pf-ERSM, LECO
2018- ABaCAS-OE
Yangtze-River-Delta
2013-2015 SMAT
2016- ICET, RSM, BenMAP-CE
2017-2018- pf-ERSM, LECO, ABaCAS-OE
Pearl-River-Delta
ABaCAS has served as a key AQ management & assessment tool for air pollution cost/benefit and attainment assessment in China
2010- RSM
2016- BenMAP-CE, SMAT
2017~2018- pf-ERSM, ICET, LECO, ABaCAS-OE
2019- Optimized pf-ERSM, FAST-CE, NEXUS
China
Jinan
Shanghai
Guangzhou
Foshan
Shenzhen
Hangzhou
Chengdu
Beijing
ABaCAS Applications in China
Notes: 补充四川