## Slide 1: The effectiveness of the “Air Pollution Prevention and Control Action Plan” on the air quality and human health during 2013-2017 in China
Jia Xing, Shuxiao Wang, Dian Ding, Jiming Hao (Tsinghua University)
Carey Jang, James Kelly (US EPA/OAQPS)
Yun Zhu (South China University of Technology)
International Aerosol Modeling Algorithms Conference, Dec 6, 2019, UC Davis

## Slide 2: Background about PM2.5 control in China
China’s air quality management has shifted from targeting “Emissions Reduction” (Technology-based) to targeting “Air Quality” (Risk-based)
Ambient air quality standards (GB 3095-2012): sets limits on PM2.5 concentration
Air Pollution Prevention and Control Action Plan: sets PM2.5 reduction target
Key questions: What are the health benefits of the action plan during 2013-2017？
What was planed
What has happened
23%
40%
BTH: Beijing-Tianjin-Hebei

## Slide 3: Anthropogenic emission reduction during 2013-2017
Chart: Emissions / kt
| 2013 | 2017 | 2013 | 2017 | 2013 | 2017 | SO2 | NOx | PM2.5
Power plants | 6792.7976 | 3010.7135 | 8800.1915 | 2429.1427 | 710.0775 | 505.0109
Industrial combustion | 6826.6247 | 4503.3414 | 2362.4896 | 1962.6297 | 1041.6433 | 703.1405
Other industry process | 2335.0601 | 1776.8139 | 2093.6579 | 2218.586 | 1013.6301 | 758.4488
Cement | 940.9594 | 933.064 | 2221.1465 | 1590.6339 | 994.5952 | 424.6435
Steel | 1042.0832 | 573.3681 | 568.9921 | 554.0416 | 1177.1059 | 549.0733
Domestic combustion | 3606.5054 | 3439.6422 | 1066.5213 | 837.2538 | 3190.8353 | 2149.3126
Transportation | 154.8399 | 176.3764 | 9640.9326 | 10515.5433 | 453.2612 | 660.8703
Open burning | 90.2449 | 77.3528 | 527.5851 | 452.2158 | 1442.8497 | 1236.7283
Controls on Power plants is effective in reducing SO2 and NOx
Primary PM reduction in industrial sectors is also important
 | SO2 | NOx | PM2.5
China | 33% | 25% | 30%
BTH | 44% | 28% | 41%
YRD | 45% | 32% | 30%
Guangdong | 37% | 20% | 18%
Sichuan-chongqing | 46% | 15% | 35%
How much percentage of the decreased PM2.5 is attributed to emission reductions?

## Slide 4: Investigation with CMAQ and ABaCAS system
Simulation scenarios (CMAQv5.2)
 | Meteorology (WRFv3.8) | Biogenic emission (MEGANv2.04) | Anthropogenic emission
① | 2013 | 2013 | 2013
② | 2017 | 2017 | 2013
③ | 2017 | 2017 | 2017
Air quality | Population | Incidence rates
①-② / ①-③ | 2013 | 2013
 | 2016 | 2013
 | 2013 | 2016
Health impact assessment (BenMAP-CE)
Data fusion (SMAT-CE)
Air quality monitoring data (2013, 2017)
Contribution of the “Air Pollution Prevention and Control Action Plan” on PM2.5 reduction and related health effects
Meteorology
Anthropogenic emission reduction
Population growth
Mortality decreases

## Slide 5: Premature deaths attribute to the change of four factors
Anthropogenic emission
Meteorology
Population
Mortality rates
The emission reduction is the dominant factor for the decrease of PM2.5 concentration and PM2.5-related premature deaths
The change of meteorology also contributes 28% of the decreased PM2.5 in BTH

## Slide 6: Premature deaths attributed to PM2.5 (2013-2017)
2013
2017
2013 - 2017
Premature deaths attribute to ambient PM2.5 in 2017 is 1102 thousands cases per year, decreased by 287 thousands (21%) from 2013.
Ding et al., EHP, 2019: Estimated Contributions of Emissions Controls, Meteorological Factors, Population Growth, and Changes in Baseline Mortality to Reductions in Ambient PM2.5 and PM2.5-Related Mortality in China, 2013–2017

## Slide 7: Background about the increase of O3 in China
PM2.5
MDA8-O3
Many factors can contribute to such increase of O3:
Meteorological variation
Emission changes
Reduced particle surface (heterogeneous reactions involving oxidants)
Aerosol direct/indirect effects on solar radiation and atmospheric dynamics
What was expected
What was unexpected
90th percentiles in maximum daily average 8-h O3
20%
25%
Key questions: What is the major driven factor for the increased O3?

## Slide 8: Anthropogenic emission reduction during 2013-2017
 | SO2 | NOx | PM2.5 | VOC
China | 33% | 25% | 30% | 4%
BTH | 44% | 28% | 41% | 12%
YRD | 45% | 32% | 30% | 4%
Guangdong | 37% | 20% | 18% | -2%
Sichuan-chongqing | 46% | 15% | 35% | 12%
Is such increased O3 related to the less/no controls on VOC?

## Slide 9: Contribution of emission and meteorology to MDA8 O3
The effects of ΔEmis-Drive compensated ΔTmet-drive, suggesting that the emission reduction are important to prevent the increase of O3
Higher temperature and stronger SW-radiation in 2017 enhances O3 formation

## Slide 10: Contribution of emission and meteorology to MDA8 O3
North
Northeast
East
Central
South
Southwest
Northwest
Tmet-drive
Emis-drive
ΔEmis-drive also varies significantly
largest benefit for O3 reduction occurs in June and July
smallest benefit or even dis-benefit in April and September

## Slide 11: Investigate the O3 response to NOx/VOC with RSM
China
(regional)
Beijing
(urban)
2017
2013
2017
2013
2017
2013
2017
2013
NOx-limited
VOC-limited
NOx-limited
VOC-limited
Strong spatial and seasonal characteristics of O3 chemistry
Ding et al., FESE, 2019: Impacts of emissions and meteorological changes on China’s ozone pollution in the warm seasons of 2013 and 2017

## Slide 12: What we learn from the Action Plan (2013-2017)?
It is effective for reducing PM2.5, but much less effective for reducing O3
How to further reduce PM2.5 to meet the national ambient air quality standard (NAAQS: 35 µg m-3), particularly in BTH?
How to reduce PM2.5 and O3 simultaneously?
Challenges:

## Slide 13: Design the optimal control pathway with LE-CO
The least-cost control strategy optimization (LE-CO) module
Response
Constraint
Cost
ICET：estimate cumulative control cost functions for each emission source;
RSM：quantify the relationship between concentration and emission reduction ratio
LECO: with certain environmental target, the optimized control ratio for each emission source can be calculated according to the minimal cost

## Slide 14: Design the optimal control pathway (pollutants)
S1: only control PM2.5
NH3 emission controls can be a cost-efficient strategy to reduce PM2.5, but not for O3
Substantial reduction on NOx and VOC is critical for simultaneous control on PM2.5 and O3
Optimal control pathway to achieve NAAQS:
S1: NOx( -5%), SO2(-75%), VOC(-25%), PM(-85%), NH3(-65%)
S2: NOx(-75%), SO2(-75%), VOC(-55%), PM(-85%), NH3(-5%)
S2: control both O3 and PM2.5
Xing et al., JEM, 2019: Least-cost control strategy optimization for air quality attainment of Beijing–Tianjin–Hebei region in China

## Slide 15: Design the optimal control pathway (seasonal)
In July, NOx control was critical because the VOC controls had little effect on either O3 or PM2.5
In January, both PM2.5 and O3 requires simultaneous VOC control to prevent the limitation of NOx controls
Control effectiveness with different NOx and VOC ratios in reducing population-weighted PM2.5 and O3 concentrations
Xing et al., ACP, 2019: Development and application of observable response indicators for design of an effective ozone and fine-particle pollution control strategy in China

## Slide 16: Source apportionment from regional emissions
Xing et al., ES&T, 2017: Quantifying Nonlinear Multiregional Contributions to Ozone and Fine Particles Using an Updated Response Surface Modeling Technique
PM2.5 (Winter)
O3 (Summer)
PM2.5
Clean
Polluted
O3
Clean
Polluted
Contribution by regional emissions increases during the heavy pollution episodes
CM: local chemistry formed by transported precursors
TP: direct transport of the pollutant from the source area to the receptor area

## Slide 17: Design the optimal control pathway (spatial)
(L:R = 1:1): the same reduction rate is applied in local and regional sources;
(L:R = 1:0.75): regional reduction rate is 75% of the local reduction rate;
(L:R = 1:0.5): regional reduction rate is half of the local reduction rate;
(L:R = 0.5:1): regional reduction rate is twice the local reduction rate;
(L:R = 1:0): only local reductions are considered)
PM2.5
O3
the same level of reductions should be conducted across the whole BTH region to achieve more aggressive targets
local reduction has priorities for attaining moderate targets

## Slide 18
Jia Xing
Associate Professor
School of Environment, Tsinghua University
Beijing, China, 10084
Email: xingjia@tsinghua.edu.cn
Thank you very much!