## Slide 1
Modelling indoor ultrafine particle dynamics
International Aerosol Modeling Algorithms Conference
Dec. 5, 2019
UC Davis
\
Donghyun Rim, Ph.D.
James L. Henderson Jr. Memorial Assistant Professor
Department of Architectural Engineering
Penn State University

## Slide 2: Indoor ultrafine particles (UFP)
  UFP sources – time varying exposure
    Outdoor
      Mobile source emissions (diesel and automobile exhaust),
      Natural nucleation bursts (gas-to-particle conversion)
    Indoor
      Combustion (gas stove, vented gas dryer, candle)
      Electric motors (power tools, blenders, hair dryers)
      High temperature process (release of SVOCs from heated surfaces)
      Chemical reaction (ozone reaction with terpene)
Source: Nazaroff & EPA

## Slide 3: UFP characteristics
  Health effects
    - Oxidative stress-induced DNA damage (Ceretti, et al. 2014, Braun et al., 2007)
    - Neurological diseases (Volk et al. 2014, Allen et al. 2014)
  Dynamic characteristics
    - Size-dependent behaviors: deposition, penetration, emission (Rim et al. 2016)
    - Concentration metrics: mass vs. surface area vs. number
    https://propertylistings.ft.com/propertynews/california/5863-five-reasons-to-live-in-berkeley-california.html
http://cweawaternews.org/sf-bay-water-board-unveils-nutrient-requirements/
Measurements are valuable, but very limited….

## Slide 4: Episodic indoor events
koreajoongangdaily.joins.com
high correlation with toxicity (Cauda et al., 2012)
cardiovascular health risk (Meier et al. 2014)
reactivity and inflammatory response (Schmid and Stoeger, 2016)
High UFP emission due to combustion
Majority of particles < 10 nm
Indoor personal exposure to UFP
Coagulation
Wallace et al.. (2008).. Environmental Science & Technology, 42(23), 8641-8647.

## Slide 5: Objectives
  Establish framework for an indoor aerosol dynamic model that estimates size-resolved behavior due to
    Particle deposition
    Coagulation
    Ventilation
    Nucleation
    Condensation/evaporation
  Consider indoor activities and building operating conditions

## Slide 6: Methods
Emission Source | Monitoring duration (min) | Total number concentration at the start of decay (cm-3) | Measured particle size range (nm) | Air exchange rate (mean±SD, h-1)
Candle | 73 | 1,100,000 | 2.33 - 63.8 | 0.04 ± 0.01
Gas stove | 178 | 305,000 | 2.17 - 63.8 | 0.14 ± 0.05
Clothes dryer | 85 | 72,000 | 9.83 - 400 | 0.36 ± 0.16
Toast | 75 | 67,000 | 10.57 - 400 | 0.34 ± 0.07
Broiled fish | 145 | 258,000 | 10.57 - 400 | 0.59 ± 0.04
Incense | 155 | 21,000 | 10.57 - 30 | 0.50 ± 0.03
  Use experimental datasets published in the literature
Wallace, L., Jeong, S.G. and Rim, D., Dynamic behavior of indoor ultrafine particles (2.3‐64 nm) due to burning candles in a residence. Indoor Air, 2019 In Press.
Rim, D., Choi, J.I. and Wallace, L.A., Size-resolved source emission rates of indoor ultrafine particles considering coagulation. Environmental science & technology, 2016, 50(18), pp.10031-10038.
Rim, D.; Green, M.; Wallace, L.; Persily, A.; Choi, J. I. Evolution of Ultrafine Particle Size Distributions Following Indoor Episodic Releases: Relative Importance of Coagulation, Deposition and Ventilation. Aerosol. Sci. Tech. 2011, 46 (5), 494-503.
Wallace, L. A. Indoor sources of ultrafine and accumulation mode particles: size distributions size-resolved concentrations and source strengths. Aerosol. Sci. Tech. 2006, 40, 348-360.

## Slide 7: Measurements data in the literature
(Gas Chromatography with Electron Capture Detector) to estimate the air change rates continuously
Wallace, L., Jeong, S.G. and Rim, D., Dynamic behavior of indoor ultrafine particles (2.3‐64 nm) due to burning candles in a residence. Indoor Air, 2019 In Press.
Rim, D., Choi, J.I. and Wallace, L.A., Size-resolved source emission rates of indoor ultrafine particles considering coagulation. Environmental science & technology, 2016, 50(18), pp.10031-10038.
Rim, D.; Green, M.; Wallace, L.; Persily, A.; Choi, J. I. Evolution of Ultrafine Particle Size Distributions Following Indoor Episodic Releases: Relative Importance of Coagulation, Deposition and Ventilation. Aerosol. Sci. Tech. 2011, 46 (5), 494-503.
Wallace, L. A. Indoor sources of ultrafine and accumulation mode particles: size distributions size-resolved concentrations and source strengths. Aerosol. Sci. Tech. 2006, 40, 348-360.
Measurements of indoor particles and ventilation
Scanning Mobility Particle Sizer (SMPS) System
Nano-DMA
GC-ECD

## Slide 8: Particle size distributions
Log-normal distribution fitting

## Slide 9
I. Log-normal distribution fitting
  II. Size and concentration dynamics
    1. Ventilation - measured
      1st order loss
    2. Particle deposition - modeled
      1st order loss
    3. Coagulation - modeled
      2nd order loss & gain

## Slide 10: Material balance model
C[m-3]: the particle number concentration for particle volumes [m3] between and at time t [s];
and : volumes of two coagulating particles;
v: volume of newly coagulated particle;
β: the coagulation kernel (collision kernel);
a: air change rate [h-1]; k: particle deposition rate [h-1];
: an involved volume (the whole house or master bedroom) [m3];
S: particle size-resolved emission rate [h-1] between and at time t.
Coagulation Gain
Losses (Deposition+ Ventilation)
Coagulation Loss Outdoor infiltration
Source emission

## Slide 11: Size-resolved coagulation kernel
Brownian+ van der Waals with 20kBT
Brownian +
Fuch correction
Brownian+ van der Waals with 200kBT
Brownian+ van der Waals with 200kBT + fractal 24nm
Rim, D., Green, M., Wallace, L., Persily, A., & Choi, J. I. (2012). Evolution of ultrafine particle size distributions following indoor episodic releases: relative importance of coagulation, deposition and ventilation. Aerosol Science and Technology, 46(5), 494-503.

## Slide 12: Iterative algorithm
To find size-resolved deposition rates
Wallace, L., Jeong, S. G., & Rim, D. (2019). Dynamic behavior of indoor ultrafine particles (2.3‐64 nm) due to burning candles in a residence. Indoor Air. 29:1018–1027

## Slide 13: Results: concentration time-series

## Slide 14: Results: concentration time-series

## Slide 15: Results: size-resolved deposition rates

## Slide 16: Results: coagulation losses
Coagulation loss rates (h-1)
0
-5
1
10
100
1000
Particle diameter (nm)
5
10
15
25
20
Candle
Gas stove
Broiled fish

## Slide 17: Results: coagulation losses
Coagulation loss rates (h-1)
0
-0.5
10
100
1000
Particle diameter (nm)
0.5
1.0
1.5
2.5
2.0
Clothes dryer
Toast
Incense

## Slide 18: Coagulation rates over time (gas stove)
Coagulation loss rates (h-1)
1
10
100
Particle diameter (nm)
-5
10
0
5
15
20
25
30
1min
3min
5min
7min
10min

## Slide 19: Relative contributions 1) coagulation 2) deposition 3) ventilation
Wallace, L., Jeong, S. G., & Rim, D. (2019). Dynamic behavior of indoor ultrafine particles (2.3‐64 nm) due to burning candles in a residence. Indoor Air. 29:1018–1027

## Slide 20: Concluding remarks
Indoor particle concentrations are log-normally distributed in size.
Coagulation and deposition is a key aerosol process for indoor aerosol concentration change and particle size distribution shift.
Coagulation can have pronounced effect during the initial decay period when the particle size is smaller at high concentrations,
Relative contributions of coagulation, deposition, and ventilation vary a function of particle size, source emission activities, and indoor conditions
Modeling can give insights into size-resolved indoor particle dynamics and exposure considering emission activities and building operating conditions.
Notes: In buildings…there are couple of ways to control indoor particles..
One of them is ventilation…
http://cbe.berkeley.edu/underfloorair/techoverview.htm we can engineer indoor climate….good news & bad news..)
- Building environmental (HVAC) systems (
Air quality - Comfort - Productivity (Wyon, Wargocki

## Slide 21: Near-human ozone and isoprene distribution
Lakey et al. (2019) The impact of clothing on ozone and squalene ozonolysis products in indoor environments. Communications Chemistry 2(1), 56.
Notes: In buildings…there are couple of ways to control indoor particles..
One of them is ventilation…
http://cbe.berkeley.edu/underfloorair/techoverview.htm we can engineer indoor climate….good news & bad news..)
- Building environmental (HVAC) systems (
Air quality - Comfort - Productivity (Wyon, Wargocki

## Slide 22: Indoor chemistry: OH- distributions
0 1×10-6 2×10-6 3×10-6 4 ×10-6 5×10-6
window
(ppb)
Fluorescent tubes CFL
Won, Y., Waring, M. S., & Rim, D. (2019). Understanding the spatial heterogeneity of indoor OH and HO2 due to photolysis of HONO using Computational Fluid Dynamics (CFD) simulation Environ. Sci. Tech. in press
Notes: In buildings…there are couple of ways to control indoor particles..
One of them is ventilation…
http://cbe.berkeley.edu/underfloorair/techoverview.htm we can engineer indoor climate….good news & bad news..)
- Building environmental (HVAC) systems (
Air quality - Comfort - Productivity (Wyon, Wargocki

## Slide 23: Back up: measurements vs. model (candle)

## Slide 24: Back up: incense

## Slide 25: Back up
LN deposition rate – 3 monotonic data (Using corrected deposition)

## Slide 26: Back up: deposition rates
Ln (particle diameter)
Ln (deposition rate)