## Slide 1
Jeffrey Pierce
Kim Sakamoto, Emily Ramnarine, Anna Hodshire
This study was supported by the U.S. National Science Foundation under Grant No. AGS-1559607, the U.S. National Oceanic and Atmospheric Administration under Grant No. NA17OAR430001, and the Joint Fire Science Program (JFSP) under Project 14-1-03-26.
Representing sub-grid biomass burning processes in regional and global models

## Slide 2: Smoke PM: complicated not just chemically… but spatially
NASA Aqua-MODIS, Pacific Northwest fires, Aug. 15, 2015.
NASA image courtesy Jeff Schmaltz, MODIS Rapid Response Team.

## Slide 3: Direct effects
NASA Aqua-MODIS, Pacific Northwest fires, Aug. 15, 2015.
NASA image courtesy Jeff Schmaltz, MODIS Rapid Response Team.

## Slide 4: Indirect effects
NASA Aqua-MODIS, Pacific Northwest fires, Aug. 15, 2015.
NASA image courtesy Jeff Schmaltz, MODIS Rapid Response Team.

## Slide 5: Concentration gradients smaller than model gridboxes
NASA Aqua-MODIS, Pacific Northwest fires, Aug. 15, 2015.
NASA image courtesy Jeff Schmaltz, MODIS Rapid Response Team.
Global-model gridbox
Regional-model gridbox

## Slide 6: Sub-grid processes affect particle mass and size distribution
POA evaporation
SOA formation
Coagulation

## Slide 7: Focus on coagulation
POA evaporation
SOA formation
Coagulation

## Slide 8: Coagulation: (1) removes number (2) increases median diameter (Dpg) (3) decreases modal width (σg)
dN/dlogDp
Dp (μm)
http://pierce.atmos.colostate.edu/apps/mphys

## Slide 9: Biomass-burning particle distributions get larger and narrower with aging
Janhäll, S., et al.:, Atmos. Chem. Phys., 10, 1427-1439, 2010.

## Slide 10: Biomass-burning particle distributions get larger and narrower with aging
Janhäll, S., et al.:, Atmos. Chem. Phys., 10, 1427-1439, 2010.
Aging

## Slide 11
3000 cm-3
1000 cm-3
dN/dlogDp
dN/dlogDp
Dp (μm)
Dp (μm)
http://pierce.atmos.colostate.edu/apps/mphys
Higher number concentration causes more coagulation

## Slide 12
3000 cm-3
1000 cm-3
dN/dlogDp
dN/dlogDp
Dp (μm)
Dp (μm)
Small Fire
Large Fire
dN/dlogDp
Dilution happens more slowly
Dilution happens more quickly
Less dilution (higher number concentration) causes more coagulation
Notes: make analogy to campfire

## Slide 13: So, how do we currently represent subgrid coagulation in models?
NASA Aqua-MODIS, Pacific Northwest fires, Aug. 15, 2015.
NASA image courtesy Jeff Schmaltz, MODIS Rapid Response Team.
Global-model gridbox
Regional-model gridbox

## Slide 14: Instantaneous mixing through the full gridbox dilutes the aerosol plume
Notes: Normally, these models immediately spread the emissions from the smoke plumes into the entire gridbox, greatly diluting the smoke

## Slide 15: Inadequate aging due to instant dilution can change the predicted size distribution
dN/dlogDp
dN/dlogDp
Dp (μm)
Dp (μm)
High Concentration
Low Concentration
Notes: More dilute emissions mean less coagulation overall (and no subgrid coagulation)

## Slide 16: Inadequate aging due to instant dilution can change the predicted size distribution
dN/dlogDp
dN/dlogDp
Dp (μm)
Dp (μm)
High Concentration
Low Concentration
How can we improve this?
Notes: More dilute emissions mean less coagulation overall (and no subgrid coagulation)

## Slide 17: Two goals for this talk
Develop a parameterization of sub-grid coagulation for regional/global models
Estimate the impact of this sub-grid coagulation on direct and indirect radiative effects

## Slide 18: Two goals for this talk
Develop a parameterization of sub-grid coagulation for regional/global models
Estimate the impact of this sub-grid coagulation on direct and indirect radiative effects

## Slide 19: Instantaneous mixing through the full gridbox dilutes the aerosol plume
Notes: Normally, these models immediately spread the emissions from the smoke plumes into the entire gridbox, greatly diluting the smoke

## Slide 20: Inadequate aging due to instant dilution can change the predicted size distribution
dN/dlogDp
dN/dlogDp
Dp (μm)
Dp (μm)
High Concentration
Low Concentration
Notes: More dilute emissions mean less coagulation overall (and no subgrid coagulation)

## Slide 21: With an in-plume coagulation parameterization, we can include the plume coagulation in the model
dN/dlogDp
Dp (μm)
Notes: What if instead of immediately diluting the plume, the model did the coagulation in the plume and then applied this size distribution to the full gridbox fire emissions

## Slide 22: We used large eddy simulation with aerosol microphysics (SAM-TOMAS) to simulate many plumes
System for Atmospheric Modelling (SAM)
Large Eddy Simulation (LES)
2D wall moving with mean wind velocity
500 m resolution
Simulate dispersion in the first 100 km from fire
TOMAS aerosol microphysics
Coagulation only
Sakamoto, K. M., Laing, J. R., Stevens, R. G., Jaffe, D. A., and Pierce, J. R.: The evolution of biomass-burning aerosol size distributions due to coagulation: dependence on fire and meteorological details and parameterization, Atmos. Chem. Phys., 16, 7709-7724, doi:10.5194/acp-16-7709-2016, 2016.

## Slide 23: We used large eddy simulation with aerosol microphysics (SAM-TOMAS) to simulate many plumes
Simulated 100 plumes varying:
Fire size
Emissions flux
Wind speed
Injection height/depth
Initial median diameter
Initial modal width
Sakamoto, K. M., Laing, J. R., Stevens, R. G., Jaffe, D. A., and Pierce, J. R.: The evolution of biomass-burning aerosol size distributions due to coagulation: dependence on fire and meteorological details and parameterization, Atmos. Chem. Phys., 16, 7709-7724, doi:10.5194/acp-16-7709-2016, 2016.

## Slide 24: Diameter increases moving downwind
Sakamoto, K. M., Laing, J. R., Stevens, R. G., Jaffe, D. A., and Pierce, J. R.: The evolution of biomass-burning aerosol size distributions due to coagulation: dependence on fire and meteorological details and parameterization, Atmos. Chem. Phys., 16, 7709-7724, doi:10.5194/acp-16-7709-2016, 2016.
Notes: Reminder of this graph

## Slide 25: A proxy for mass concentration captures much of the model variability
Sakamoto, K. M., Laing, J. R., Stevens, R. G., Jaffe, D. A., and Pierce, J. R.: The evolution of biomass-burning aerosol size distributions due to coagulation: dependence on fire and meteorological details and parameterization, Atmos. Chem. Phys., 16, 7709-7724, doi:10.5194/acp-16-7709-2016, 2016.
Proxy for initial mass concentration
Notes: Reminder of this graph

## Slide 26: Modal width depends greatly on the initial value, but the mass concentration determines the rate of change
Sakamoto, K. M., Laing, J. R., Stevens, R. G., Jaffe, D. A., and Pierce, J. R.: The evolution of biomass-burning aerosol size distributions due to coagulation: dependence on fire and meteorological details and parameterization, Atmos. Chem. Phys., 16, 7709-7724, doi:10.5194/acp-16-7709-2016, 2016.
Proxy for initial mass concentration
Notes: Reminder of this graph

## Slide 27: Parameterization fit to these simulations
Sakamoto, K. M., Laing, J. R., Stevens, R. G., Jaffe, D. A., and Pierce, J. R.: The evolution of biomass-burning aerosol size distributions due to coagulation: dependence on fire and meteorological details and parameterization, Atmos. Chem. Phys., 16, 7709-7724, doi:10.5194/acp-16-7709-2016, 2016.
Notes: To be used for single fire
(fit A, b, and c to this plot)

## Slide 28: Tested the fits against aged biomass burning size measurements from Mt. Bachelor
Red: main parameterization
R2 = 0.55
Sakamoto, K. M., Laing, J. R., Stevens, R. G., Jaffe, D. A., and Pierce, J. R.: The evolution of biomass-burning aerosol size distributions due to coagulation: dependence on fire and meteorological details and parameterization, Atmos. Chem. Phys., 16, 7709-7724, doi:10.5194/acp-16-7709-2016, 2016.
Blue: different fit (not presented here)

## Slide 29: Two goals for this talk
Develop a parameterization of sub-grid coagulation for regional/global models
Estimate the impact of this sub-grid coagulation on direct and indirect radiative effects

## Slide 30: Estimate the global effects using GEOS-Chem TOMAS
Chemical Transport Model
• 4x5° horizontal resolution
• 47 vertical layers
TOMAS
GEOS-5 meteorology
Fire emissions: GFED4 or FINN
TwO-Moment Aerosol Sectional (TOMAS) microphysics
• Tracks mass and number
• 15 size bins 3nm-10 μm
Direct effect and cloud-albedo indirect effects through RRTMG
Ramnarine, E., Kodros, J. K., Hodshire, A. L., Lonsdale, C. R., Alvarado, M. J., and Pierce, J. R.: Effects of Near-Source Coagulation of Biomass Burning Aerosols on Global Predictions of Aerosol Size Distributions and Implications for Aerosol Radiative Effects, Atmos. Chem. Phys., https://doi.org/10.5194/acp-2018-1084, 2019.

## Slide 31: Test with and without subgrid coagulation
Ramnarine, E., Kodros, J. K., Hodshire, A. L., Lonsdale, C. R., Alvarado, M. J., and Pierce, J. R., Effects of Near-Source Coagulation of Biomass Burning Aerosols on Global Predictions of Aerosol Size Distributions and Implications for Aerosol Radiative Effects, Atmos. Chem. Phys., https://doi.org/10.5194/acp-2018-1084, 2019.
Chemical Transport Model
• 4x5° horizontal resolution
• 47 vertical layers
TOMAS
GEOS-5 meteorology
Fire emissions: GFED4 or FINN
TwO-Moment Aerosol Sectional (TOMAS) microphysics
• Tracks mass and number
• 15 size bins 3nm-10 μm
Direct effect and cloud-albedo indirect effects through RRTMG

## Slide 32: Global N10 (Dp > 10 nm) and N80 (Dp > 80 nm) without biomass burning
N10
N80
Global =
%
Global =
%
Global =
%
Global =
%
Surface concentrations w/o biomass burning
No sub-grid coag.
All BB emissions
Dpg=100 nm, σg=2.0
With sub-grid coagulation
Ramnarine, E., Kodros, J. K., Hodshire, A. L., Lonsdale, C. R., Alvarado, M. J., and Pierce, J. R., Effects of Near-Source Coagulation of Biomass Burning Aerosols on Global Predictions of Aerosol Size Distributions and Implications for Aerosol Radiative Effects, Atmos. Chem. Phys., https://doi.org/10.5194/acp-2018-1084, 2019.
Notes: Now we are switching gears from emitted size distribution to ambient size distribution. On the left we have the number of particles per m2 above 10nm (top) and 80nm (bottom) without any biomass burning aerosols. This is for reference. On the right we can see the percent change in aerosol number concentration when we add in biomass burning aerosols. We can see that there is always an increase in the number of particles. Here we can see some key biomass burning regions and the areas downwind are most effected. On the right-hand figure we have the panel on the left that does not have subgrid coagulation and represents the model by default. On the right we have the same run but with subgrid coagulation added using the parameterization discussed. We can see that there is a general decrease in the number of particles when subgrid coagulation is added, especially in the Amazon and Congo regions. We can also see that a smilar change occurs in N10 as in N80.

## Slide 33: Adding biomass burning increases CCN-sized particles (N80) by ~15%
N10
N80
Global =
%
Global =
%
Global =
%
Global =
%
Surface concentrations w/o biomass burning
No sub-grid coag.
All BB emissions
Dpg=100 nm, σg=2.0
With sub-grid coagulation
Ramnarine, E., Kodros, J. K., Hodshire, A. L., Lonsdale, C. R., Alvarado, M. J., and Pierce, J. R., Effects of Near-Source Coagulation of Biomass Burning Aerosols on Global Predictions of Aerosol Size Distributions and Implications for Aerosol Radiative Effects, Atmos. Chem. Phys., https://doi.org/10.5194/acp-2018-1084, 2019.
Notes: Now we are switching gears from emitted size distribution to ambient size distribution. On the left we have the number of particles per m2 above 10nm (top) and 80nm (bottom) without any biomass burning aerosols. This is for reference. On the right we can see the percent change in aerosol number concentration when we add in biomass burning aerosols. We can see that there is always an increase in the number of particles. Here we can see some key biomass burning regions and the areas downwind are most effected. On the right-hand figure we have the panel on the left that does not have subgrid coagulation and represents the model by default. On the right we have the same run but with subgrid coagulation added using the parameterization discussed. We can see that there is a general decrease in the number of particles when subgrid coagulation is added, especially in the Amazon and Congo regions. We can also see that a smilar change occurs in N10 as in N80.

## Slide 34: Subgrid coagulation reduces the impact of biomass burning on N10 and N80
N10
N80
Global =
%
Global =
%
Global =
%
Global =
%
Surface concentrations w/o biomass burning
No sub-grid coag.
All BB emissions
Dpg=100 nm, σg=2.0
With sub-grid coagulation
Ramnarine, E., Kodros, J. K., Hodshire, A. L., Lonsdale, C. R., Alvarado, M. J., and Pierce, J. R., Effects of Near-Source Coagulation of Biomass Burning Aerosols on Global Predictions of Aerosol Size Distributions and Implications for Aerosol Radiative Effects, Atmos. Chem. Phys., https://doi.org/10.5194/acp-2018-1084, 2019.
Notes: Now we are switching gears from emitted size distribution to ambient size distribution. On the left we have the number of particles per m2 above 10nm (top) and 80nm (bottom) without any biomass burning aerosols. This is for reference. On the right we can see the percent change in aerosol number concentration when we add in biomass burning aerosols. We can see that there is always an increase in the number of particles. Here we can see some key biomass burning regions and the areas downwind are most effected. On the right-hand figure we have the panel on the left that does not have subgrid coagulation and represents the model by default. On the right we have the same run but with subgrid coagulation added using the parameterization discussed. We can see that there is a general decrease in the number of particles when subgrid coagulation is added, especially in the Amazon and Congo regions. We can also see that a smilar change occurs in N10 as in N80.

## Slide 35: What do the size distributions look like in smoke-impacted regions?
We will focus on two interesting grid boxes
N10
N80
Surface concentrations w/o biomass burning
No sub-grid coag.
All BB emissions
Dpg=100 nm, σg=2.0
With sub-grid coagulation
Global =
%
Global =
%
Global =
%
Global =
%
Ramnarine, E., Kodros, J. K., Hodshire, A. L., Lonsdale, C. R., Alvarado, M. J., and Pierce, J. R., Effects of Near-Source Coagulation of Biomass Burning Aerosols on Global Predictions of Aerosol Size Distributions and Implications for Aerosol Radiative Effects, Atmos. Chem. Phys., https://doi.org/10.5194/acp-2018-1084, 2019.
Notes: Now we are switching gears from emitted size distribution to ambient size distribution. On the left we have the number of particles per m2 above 10nm (top) and 80nm (bottom) without any biomass burning aerosols. This is for reference. On the right we can see the percent change in aerosol number concentration when we add in biomass burning aerosols. We can see that there is always an increase in the number of particles. Here we can see some key biomass burning regions and the areas downwind are most effected. On the right-hand figure we have the panel on the left that does not have subgrid coagulation and represents the model by default. On the right we have the same run but with subgrid coagulation added using the parameterization discussed. We can see that there is a general decrease in the number of particles when subgrid coagulation is added, especially in the Amazon and Congo regions. We can also see that a smilar change occurs in N10 as in N80.

## Slide 36: Sub-grid coagulation shifts size distribution in locations dominated by smoke
Ramnarine et al., 2019
Alaska
Amazon

## Slide 37: Biomass burning radiative effects: Subgrid coag decreases AIE Subgrid coag slightly increases DRE
Ramnarine et al., 2019

## Slide 38: Primary organic aerosol (POA) evaporation vs. secondary organic aerosol (SOA) formation: Net increase or decrease in PM2.5?
POA evaporation
SOA formation
Coagulation

## Slide 39: Organic aerosol is semivolatile: Evaporates as smoke dilutes
Distance
OA
CO
Primary OA ratio to CO at emissions

## Slide 40: Big fires vs. small fires… impacts dilution
NASA Aqua-MODIS, Pacific Northwest fires, Aug. 15, 2015.
NASA image courtesy Jeff Schmaltz, MODIS Rapid Response Team.

## Slide 41: Big fires dilute more slowly… expect less evaporation?
Distance
OA
CO
Big fire
Small fire

## Slide 42: Chemistry: Secondary Organic Aerosol (SOA) formation may increase mass
Distance
OA
CO
Dilution/evaporation only
Dilution/evaporation + chemistry/condensation

## Slide 43: Evaporation vs. SOA formation… What wins overall?
Distance
OA
CO
Small fire: Evaporation only
Big fire: Evaporation only
Small fire: Evap+SOA
Big fire: Evap+SOA

## Slide 44: How to represent these processes in 3D models?
POA evaporation
SOA formation
Coagulation
Working towards this…
Anna Hodshire’s talk next!

## Slide 45: Questions

## Slide 46: Extras

## Slide 47: Biomass burning contributes significantly to ambient aerosol number regardless of subgrid coagulation
We will focus on two interesting grid boxes
N10
N80
Surface concentrations w/o biomass burning
No sub-grid coag.
All BB emissions
Dpg=100 nm, σg=2.0
With sub-grid coagulation
Global =
%
Global =
%
Global =
%
Global =
%
Ramnarine, E., Kodros, J. K., Hodshire, A. L., Lonsdale, C. R., Alvarado, M. J., and Pierce, J. R., Effects of Near-Source Coagulation of Biomass Burning Aerosols on Global Predictions of Aerosol Size Distributions and Implications for Aerosol Radiative Effects, Atmos. Chem. Phys., https://doi.org/10.5194/acp-2018-1084, 2019.
Notes: Now we are switching gears from emitted size distribution to ambient size distribution. On the left we have the number of particles per m2 above 10nm (top) and 80nm (bottom) without any biomass burning aerosols. This is for reference. On the right we can see the percent change in aerosol number concentration when we add in biomass burning aerosols. We can see that there is always an increase in the number of particles. Here we can see some key biomass burning regions and the areas downwind are most effected. On the right-hand figure we have the panel on the left that does not have subgrid coagulation and represents the model by default. On the right we have the same run but with subgrid coagulation added using the parameterization discussed. We can see that there is a general decrease in the number of particles when subgrid coagulation is added, especially in the Amazon and Congo regions. We can also see that a smilar change occurs in N10 as in N80.

## Slide 48: Sub-grid coagulation shifts size distribution in locations dominated by smoke
Ramnarine et al., 2019

## Slide 49: Gas-phase chemistry may shift mass to lower volatility, create SOA
Shift organic mass to lower volatility?

## Slide 50: Qualitative results consistent across a wide range of sensitivity tests
Ramnarine et al., 2019

## Slide 51: Observed plumes show variability in net OA production/evaporation
Cubison, M. J., et al.: Effects of aging on organic aerosol from open biomass burning smoke in aircraft and laboratory studies, Atmos. Chem. Phys., 11(23), 12049–12064, 2011.

## Slide 52: Condensation: (1) conserves number (2) increases median diameter (Dpg) (3) decreases modal width (σg)

## Slide 53: Biomass-burning particle distributions get larger and narrower with aging
Janhäll, S., et al.:, Atmos. Chem. Phys., 10, 1427-1439, 2010.
Aging
Is this coagulation or SOA production?
BOTH should increase diameter and narrow distribution

## Slide 54: HUGE range in fire sizes
10-5 10-4 10-3 10-2 10-1 100 101 102 103
Fire area [km2 blackened day-1]
100
101
102
103
104
Number of fires in US in 2014
US Fires for 2014 from EPA NEI

## Slide 55: HUGE range in fire sizes
10-5 10-4 10-3 10-2 10-1 100 101 102 103
Fire area [km2 blackened day-1]
100
101
102
103
104
Number of fires in US in 2014
US Fires for 2014 from EPA NEI

## Slide 56: How do fire size, dilution rate, and background concentration matter?

## Slide 57: How do fire size, dilution rate, and background concentration matter?
How do these factors impact:
aerosol mass?
size distribution?
CCN?
extinction?

## Slide 58: Road map
Aging processes affect size distributions
  POA evaporation vs. SOA formation vs. coagulation?
  How much do fire size and background concentration matter?
The impact of in-plume coagulation on global radiative effects

## Slide 59: Road map
Aging processes affect size distributions
  POA evaporation vs. SOA formation vs. coagulation?
  How much do fire size and background concentration matter?
The impact of in-plume coagulation on global radiative effects
Anna Hodshire

## Slide 60
Center line
2*σy
Wind (U, m/s)
2*σz
x
4σy
Q
4σz
Investigating OA in expanding plumes
Plume volume expansion: Gaussian-dispersion framework
  Fire areas: 1×10-4 (small prescribed fire) through 1×102 km2 (large wildfires)
  Background OA concentrations: 0, 5, 20, 50 µg m-3
  Atmospheric stability class : D (neutral) (tested others, not shown)
  OA emissions mass flux: 5×10-6 kg m-2 s-1
Notes: We apply a simple Gaussian-dispersion framework to represent plume volume expansion in our box model. We assume that the pollutants are uniformly distributed within a box with a crosswind width of y ± 2σy and height z ± 2σz (the thickness of the box in the wind direction is fixed at 1 m), so that the plume volume in the simulation is 4σy×4 σy×1 m3. We assume that the initial plume width (σy) is the same as the fire width (the square root of the fire area). The background is considered to be non-volatile OA with a fixed concentration of 5 µg m-3.
We perform sensitivity tests for fire areas of 1×10-4, 1×10-2, 1 and 1×102 km2 . The smallest fire size (1×10-4 km2) was selected to represent a prescribed fire and the larger fire sizes (1 and 1×102 km2) represent wildfire sources. For a fire size of 1 km2, we also test the sensitivity to atmospheric stability class (A (unstable), D (neutral) and F (stable)) for mass fluxes of 2×10-8 and 5×10-6 kg m-2 s-1. The dispersion parameters used to estimate σy and σz for different Pasquill stability classes are taken from Klug (1969).

## Slide 61
36 logarithmically spaced size, 3 nm to 10 µm
Smoke emissions: Single lognormal mode w/ Dpm = 160 nm, σg = 1.7
Number size distribution
Mass size distribution
TwO-Moment Aerosol Sectional (TOMAS) microphysics
Notes: This slide lists the TOMAS model and other parameter setting for the base simulation

## Slide 62
TwO-Moment Aerosol Sectional (TOMAS) microphysics
36 logarithmically spaced size, 3 nm to 10 µm
Smoke emissions: Single lognormal mode w/ Dpm = 160 nm, σg = 1.7
Black carbon, water and 15 lumped organics with logarithmically spaced Ci* (10-3 to 104)
Number size distribution
Mass size distribution
Based on FLAME-4 GC measurements
Based on FLAME-3 thermodenuder measurements
Bian et al. (2017)
Notes: This slide lists the TOMAS model and other parameter setting for the base simulation

## Slide 63
Simple gas-phase chemistry mechanism (Jathar et al. 2014)
All functionalization, no fragmentation
Assumption 1: Fast chemistry (upper bound of SOA production)
  Rate constants based on aromatics
  4 volatility-bin drop per reaction
  OH = 1x106 molec cm-3
Assumption 2: Slow chemistry (lower bound of SOA production)
  Rate constants based on alkanes
  2 volatility-bin drop per reaction
Notes: The gas-phase organic chemistry matrix used in the model follows the study of Jathar et al. (2014). We assume that only functionalization occurs in the biomass-burning experiments, with the product organic vapors having volatilities that are either 2 or 4 volatility bins lower than the parent. a represents for the fast chemistry (4 volatility bins drop) and b for the slow chemistry (2 volatility bins drops).

## Slide 64: How much do OA evap, SOA formation, and coagulation matter?
Sets of simulations
  Coag: On / Off
  SOA chemistry: On / Off
  (Dilution / evaporation on in every simulations)

## Slide 65: How much do OA evap, SOA formation, and coagulation matter?
Sets of simulations
  Coag: On / Off
  SOA chemistry: On / Off
  (Dilution / evaporation on in every simulations)

## Slide 66: Dilution spans orders of magnitude depending on fire size
Time [hr]
Dilution Ratio

## Slide 67: Dilution greatly influences smoke concentrations!
Time [hr]
Time [hr]
PM concentration with background of 0 μg m-3
Dilution Ratio

## Slide 68: How does smoke mass age?
after 4 hours
Background concentration
Fire size

## Slide 69: How does smoke mass age?
after 4 hours
Background concentration
Fire size

## Slide 70: In absence of chemistry: - Fires lose mass by OA evaporation - Smaller fires evaporate more (more dilution) - Polluted background slows evaporation
after 4 hours
Background concentration
Fire size

## Slide 71: With chemistry: - SOA production exceeds evaporation (net OA production) for all but small fires in clean backgrounds
after 4 hours
Background concentration
Fire size

## Slide 72: We expect fire size and background to matter…

## Slide 73: What about shifts in the size distribution?
Janhäll, S., et al.:, Atmos. Chem. Phys., 10, 1427-1439, 2010.
Aging

## Slide 74: Size distribution changes for large fires - Both SOA and coagulation make distribution larger and narrower - Coagulation has slightly larger effect
100 km2 fire, polluted background
after 4 hours

## Slide 75: Size distribution changes: - Coagulation makes distribution larger and smaller for large fires - SOA production has similar effect - Evaporation makes distribution smaller but not wider
after 4 hours

## Slide 76: How do CCN(0.2%) change in the plume?
Background concentration
Fire size
after 4 hours

## Slide 77: CCN(0.2%): Dilution/Evap: decrease CCN (background OA slows evaporation)
Background concentration
Fire size
after 4 hours

## Slide 78: CCN(0.2%): Coagulation kills CCN for big fires
Background concentration
Fire size
after 4 hours

## Slide 79: CCN(0.2%): SOA increases CCN (growing ultrafine particles)
Background concentration
Fire size
after 4 hours

## Slide 80: CCN(0.2%): Overall: Coag death wins for big fires SOA production wins for small fires
Background concentration
Fire size
after 4 hours

## Slide 81: Extinction: Similar to OA mass changes, but coagulation increase extinction for large fires
Background concentration
Fire size
after 4 hours

## Slide 82: Mass again
after 4 hours
Background concentration
Fire size

## Slide 83: Coagulation pushes mass to sizes with higher mass-scattering efficiency

## Slide 84: When do we expect processes to dominate?
Background concentration
Background concentration

## Slide 85: Fires by number…
10-5 10-4 10-3 10-2 10-1 100 101 102 103
Fire area [km2 blackened day-1]
100
101
102
103
104
Number of fires in US in 2014
US Fires for 2014 from EPA NEI

## Slide 86: Fires by number… and weighted by area
Proxy for emissions
US Fires for 2014 from EPA NEI

## Slide 87: Fires by number… and weighted by area
Most field campaigns
Proxy for emissions
US Fires for 2014 from EPA NEI

## Slide 88: Two take-home points
Fire size and meteorological factors very important for plume aging.
Global/regional models can’t resolve plumes… need sub-grid representation.

## Slide 89: The big caveat
Need to test both parts of results on measurements…
  (challenging to do)

## Slide 90: OA evaporates in diluting plumes: Same phenomena as evaporating contrails
Distance
H2Oice
CO

## Slide 91: Organic aerosol evaporation as smoke dilutes: Like contrails… but a multi-species system
Donahue et al., Atmospheric organic particulate matter: From smoke to secondary organic aerosol, Atmos. Env., 2008
White: organics in gas phase
Green: organics in aerosol phase
Low volatility
High volatility

## Slide 92
Donahue et al., Atmospheric organic particulate matter: From smoke to secondary organic aerosol, Atmos. Env., 2008
White: organics in gas phase
Green: organics in aerosol phase
Low volatility
High volatility
Low volatility
High volatility
Dilute by factor of 18
OA reduced by factor of 100
Organic aerosol evaporation as smoke dilutes: Like contrails… but a multicomponent system

## Slide 93: Organic aerosol is semivolatile: Evaporates as smoke dilutes
Distance
OA
CO
Primary OA ratio to CO at emissions